## Slide 1
Learning the pulling response of a soft actuator
A machine-learning study of pressure, displacement, and compliant materials
SOFT ROBOTICS · MACHINE LEARNING · HAREHARAN B T
P
pulling
response
Notes: Project proposal based on the EPFL soft-actuator force-characterization dataset. Source: Joshi and Paik, IEEE Robotics and Automation Letters (2019), DOI: 10.1109/LRA.2019.2927936; dataset DOI: 10.5281/zenodo.3627901.

## Slide 2
Material structure and loading
A soft actuator’s mechanics emerge from its compliant body and its constraints
air pressure
fabric layer limits extension
pressurized chambers
Elastomer body
Deforms under pneumatic pressure and bends around contact or load constraints.
Fabric constraint
Restricts extension on one side, producing bending instead of uniform expansion.
Our ML target is the actuator’s pulling response under imposed displacement.
Notes: The paper describes a soft bending actuator with a fabric layer that prevents extension on one side when pressurized. The pulling-force tests constrain its two ends and impose linear displacement. Source: Joshi and Paik, 2019, DOI: 10.1109/LRA.2019.2927936.

## Slide 3
Question and experimental data
A real, repeated measurement set gives the model a mechanical response to learn
RESEARCH QUESTION
Can pressure and imposed displacement predict the actuator’s pulling response?
DATASET
EPFL soft-actuator force characterization
9
pressure settings
0–200 kPa
30
recorded trials
3–4 repeats per setting
37,073
aligned rows
within shared time range
One actuator and one test setup; the dataset does not cover multiple elastomer formulations.
Notes: Zenodo describes three raw-data archives and MATLAB plotting scripts. We use the pulling-force subset. The paper reports nine pressure levels from 0 to 200 kPa in 25 kPa steps; each level has three repetitions, with some conditions having a fourth. After aligning sensor samples to the supplied position trajectory over their shared time range, 37,073 rows remain. Sources: https://zenodo.org/records/3627901 and Joshi and Paik, DOI: 10.1109/LRA.2019.2927936.

## Slide 4
From raw recordings to model inputs
The model learns a mapping from operating conditions to a measured response
Pressure
measured kPa
Displacement
normalized 0–1
Regression model
quadratic features
Output
horizontal sensor counts
Pulling response = sign-corrected mean of the two opposing horizontal readings (modules 1 and 3).
Important: target remains in raw sensor counts. The downloadable archive does not include the load-cell calibration factors needed to report newtons.
Notes: The raw recording matrices have eight columns and no headers. The final column is measured pressure; the first is a sample time/index. The six middle channels correspond to the three biaxial load-cell modules described in the paper. The authors define pulling force as the mean horizontal force from modules 1 and 3 with sign conventions; because the archive omits their plotting/calibration helper, this project reports the sign-corrected sensor signal in counts, not newtons. Position is aligned by interpolation over the shared time window and normalized to the trajectory maximum. Sources: Zenodo DOI 10.5281/zenodo.3627901; Joshi and Paik, DOI 10.1109/LRA.2019.2927936.

## Slide 5
Leave-one-pressure-level-out validation
All trials at one pressure setting are held out together for each fold
ONE FOLD
0
kPa
25
kPa
50
kPa
75
kPa
100
kPa
125
kPa
150
kPa
175
kPa
200
kPa
TRAIN: the other 8 levels
TEST: the remaining level
Repeat nine times, rotating the held-out pressure level. This evaluates interpolation within the tested range—not transfer to a different actuator.
Notes: The final evaluation uses LeaveOneGroupOut with pressure setpoint as the group: all trials at a setting are withheld together; each of the nine settings is held out once. This prevents the model from seeing other trials at the same pressure setting in that fold. It tests interpolation between measured levels in this one actuator setup, not device or material transfer. The protocol's nine setpoints are from Joshi and Paik, DOI: 10.1109/LRA.2019.2927936.

## Slide 6
Quadratic models lead pressure-level validation
Each of the nine pressure settings is held out once; all 37,073 aligned rows contribute to pooled scores
Pooled R² across nine folds
Chart: 
| Linear | Random forest | Quadratic | Quadratic ridge
R² | 0.758 | 0.76 | 0.901 | 0.901
Quadratic
Ridge
MEAN ABSOLUTE ERROR
135.5 counts
RMSE 168.6 counts · R² 0.901
Quadratic ridge edges quadratic OLS by just 0.03 counts RMSE. Counts are not newtons.
Notes: Leave-one-pressure-level-out pooled results over all 37,073 rows: linear regression R² 0.757725, MAE 205.366 counts, RMSE 263.081 counts; quadratic regression R² 0.900513, MAE 135.512 counts, RMSE 168.585 counts; random forest R² 0.760219, MAE 211.756 counts, RMSE 261.724 counts; quadratic ridge R² 0.900547, MAE 135.495 counts, RMSE 168.556 counts. Quadratic ridge has the lowest RMSE, but the difference from unregularized quadratic regression is negligible (0.029 counts). Selected model saved after fitting all prepared rows. Target remains uncalibrated load-cell counts. Dataset source: https://zenodo.org/records/3627901.

## Slide 7
Validation varies by pressure level
Pooled accuracy is useful, but it does not imply equal performance at every setting
R² when each pressure level is held out
Chart: 
| 0 | 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200
Quadratic ridge | -0.194 | 0.646 | 0.018 | 0.637 | 0.942 | 0.774 | 0.774 | 0.932 | 0.899
Fold-level insight
The 0 and 50 kPa folds are much harder to predict than most middle and high pressure folds.
Interpretation
The two quadratic models are essentially tied. These results apply to one actuator and one setup; they do not establish material-independent behavior.
Notes: Per-pressure R² values for the selected Quadratic Ridge model, in kPa order 0,25,50,75,100,125,150,175,200: -0.194, 0.646, 0.018, 0.637, 0.942, 0.774, 0.774, 0.932, 0.899. The pooled score masks difficult folds at 0 and 50 kPa. Quadratic Ridge and unregularized quadratic regression differ by only 0.029 counts in pooled RMSE, so the winner should not be interpreted as a meaningful advantage. Source: project leave-one-pressure-level-out analysis of the Zenodo pulling-force subset.

## Slide 8
Next steps
Turn a promising fit into a defensible robotics result
01
Recover calibration
Convert load-cell outputs to newtons from the original calibration data.
02
Validate alignment
Check pressure, position, and force timestamps against the source plotting workflow.
03
Test a new actuator run
Compare predictions with a physical run at a pressure not used for training.
04
Try inverse design
Use the validated model to estimate pressure for a target pulling response.
Notes: The first two steps are needed before quoting force in newtons or presenting the model as a calibrated physical predictor. A physical validation trial would strengthen the ML project. Inverse design is a future extension, not a result of the current analysis.

## Slide 9
Sources
Dataset and experiment used in this project
1
Joshi, S. & Paik, J. (2019). Multi-DoF Force Characterization of Soft Actuators. IEEE Robotics and Automation Letters, 4(4), 3679–3686.
DOI: 10.1109/LRA.2019.2927936
2
Joshi, S. & Paik, J. Dataset for “Multi-DoF Force Characterization of Soft Actuators.” Zenodo (2020).
DOI: 10.5281/zenodo.3627901 · https://zenodo.org/records/3627901
Model metrics are calculated from the downloaded pulling-force subset; sensor targets are reported in raw counts pending calibration.
Notes: Full source citations: Joshi, S. D. and Paik, J., ‘Multi-DoF Force Characterization of Soft Actuators,’ IEEE Robotics and Automation Letters, vol. 4, no. 4, pp. 3679–3686, 2019, DOI 10.1109/LRA.2019.2927936. Dataset: https://zenodo.org/records/3627901, DOI 10.5281/zenodo.3627901. Model metrics are computed with the project analysis script from the pulling-force subset.